## Slide 1
Static Routing Implementation
Cisco Confidential

## Slide 2: Reach Remote Networks
Static Routing
A router can learn about remote networks in one of two ways:
Manually - Remote networks are manually entered into the route table using static routes.
Dynamically - Remote routes are automatically learned using a dynamic routing protocol.
  RIP v2
  EIGRP
  OSPF
Cisco Confidential

## Slide 3: Why Use Static Routing?
Static Routing
Static routing provides some advantages over dynamic routing, including:
Static routes are not advertised over the network, resulting in better security.
Static routes use less bandwidth than dynamic routing protocols, no
CPU cycles are used to calculate and communicate routes.
The path a static route uses to send data is known.
Cisco Confidential

## Slide 4: When to Use Static Routes
Static Routing
Static routing has three primary uses:
Providing ease of routing table maintenance in smaller networks.
Routing to and from stub networks. A stub network is a network
accessed by a single route, and the router has no other neighbors.
Using a single default route to represent a path to any network that does not have a more specific match with another route in the routing table.
Cisco Confidential

## Slide 5: Static Route Applications
Types of Static Routes
Cisco Confidential
Static Routes are often used to:
Connect to a specific network.
Provide a Gateway of Last Resort for a stub network.
Reduce the number of routes advertised by summarizing several contiguous networks as one static route.
Create a backup route in case a primary route link fails.

## Slide 6: Types of Static Routes Standard Static Route
Cisco Confidential

## Slide 7: Default Static Route
© 2008 Cisco Systems, Inc. All rights reserved. Cisco Confide
Types of Static Routes
A default static route is a route that matches all packets.
A default route identifies the gateway IP address to which the router
sends all IP packets that it does not have a learned or static route.
A default static route is simply a static route with 0.0.0.0/0 as the destination IPv4 address.
ntial

## Slide 8: Types of Static Routes Summary Static Route
Cisco Confidential

## Slide 9: Types of Static Routes Floating Static Route
Cisco Confidential

## Slide 10
6.2 Configure Static and Default Routes
Cisco Confidential

## Slide 11: Configure IPv4 Static Routes
ip route Command
Cisco Confidential

## Slide 12: Next-Hop Options
Configure IPv4 Static Routes
Cisco Confidential
The next hop can be identified by an IP address, exit interface, or both. How the destination is specified creates one of the three following route types:
Next-hop route - Only the next-hop IP address is specified.
Directly connected static route - Only the router exit interface is specified.
Fully specified static route - The next-hop IP address and exit interface are specified.

## Slide 13: Configure IPv4 Static Routes Configure a Next-Hop Static Route
Cisco Confidential

## Slide 14: Configure IPv4 Static Routes Configure Directly Connected Static Route
Cisco Confidential

## Slide 15: Configure IPv4 Static Routes Configure a Fully Specified Static Route
Cisco Confidential

## Slide 16: Configure IPv4 Static Routes Verify a Static Route
Cisco Confidential

## Slide 17: Configure IPv4 Static Routes Default Static Route
Cisco Confidential

## Slide 18: Configure IPv4 Static Routes Configure a Default Static Route
© 2008 Cisco Systems, Inc. All rights reserved. Cisco Confidential

## Slide 19: Configure IPv4 Static Routes Verify a Default Static Route
Verify a Default Static Route Verify a Default Static Route
Cisco Confidential